## Slide 1: Terroir and Drought in the Anderson Valley
Zac Robinson
April 2022

## Slide 2: A Different Landscape
Anderson Valley is physically different from Inland Mendocino
climate
terrain / soils
isolated
water sources
presence of endangered species (Coho)
TERROIR

## Slide 3: Good Rainfall
TERROIR
Source: Krisweb/Oregon State

## Slide 4: Vineyards Are Different
Because AV is physically different, our vineyards look different:
smaller (median 13 acres)
hillside
modern
singular varietal focus
TERROIR

## Slide 5: Hillsides, small blocks
TERROIR

## Slide 6: What is Water “Security”?
Water security per United Nations definition
“The capacity of a population to safeguard sustainable access to adequate quantities of acceptable quality water for sustaining livelihoods, human well-being, and socio-economic development, for ensuring protection against water-borne pollution and water-related disasters, and for preserving ecosystems in a climate of peace and political stability.”
Water security per this farmer:
“Enough water to farm this year.”
WATER
SECURITY

## Slide 7: Inland Water Security
Inland Mendocino water security can include
surface water diversion
contract with RRFC
purple pipe in Ukiah Valley
Potter Valley project
wells
winter collection to ponds
WATER
SECURITY

## Slide 8: Anderson Valley Water Security
In Anderson Valley the options for water security
are much more limited
surface water diversion
contract with RRFC
purple pipe in Ukiah Valley
Potter Valley project
wells
winter collection to ponds
WATER
SECURITY

## Slide 9: Analysis of AV Vineyard Water Security
WATER
SECURITY

## Slide 10: Getting More From Our Ponds
Reduce Demand
Irrigation efficiency
Alternative methods of frost protection
Increase Supply
Reduce leakage
Reduce evaporation
REDUCE
DEMAND

## Slide 11: Demand Reduction - Efficiency
We improve water security when we reduce
our demand for water.
Modern/efficient drip irrigation systems
  Dual drip lines
  Soil moisture monitoring
Precision irrigation
  Smaller blocks
REDUCE
DEMAND

## Slide 12: Demand Reduction – Frost Nights
Anderson Valley is re-discovering wind machines for light frost events. Installations can be budgeted like a water purchase. One case study:
$100k investment
20 acres
two annual frost events for 10 years
= 254 acre feet of water saved
=$400/AF
REDUCE
DEMAND

## Slide 13: Getting More From Our Ponds
Demand Reduction
Irrigation efficiency
Alternative methods of frost protection
Increase Supply 
Reduce leakage
Reduce evaporation
INCREASE
SUPPLY

## Slide 14: Supply Improvements – Pond Liners
Projects to reduce pond losses can be budgeted like buying water. One recent liner installation of a 3 AF pond
$60k investment
2 AF annual leakage
assume 30 years of life
= 60 acre feet of water saved
=$1000/AF
INCREASE
SUPPLY

## Slide 15: Old Pond, New Liner
INCREASE
SUPPLY

## Slide 16: Evaporative Losses
In the winery, evaporative losses are “The Devil’s Share.” The same applies to the vineyard.
1/3 inch on a hot breezy summer day!
3 ft over a typical summer
In an example pond this is 34% loss of storage
INCREASE
SUPPLY

## Slide 17: Evaporation Research
Evaporation from surface water is controlled
by many factors. The simple list includes:
Air temp and humidity
Water temp
Wind speed
Reservoir geometry
INCREASE
SUPPLY

## Slide 18: Evaporation Research
Factors we can control for our ponds.
Air temp and humidity
Water temp
Wind speed
Reservoir geometry
INCREASE
SUPPLY

## Slide 19: Reducing the “Devils Share”
Reduce your surface water temperature
Shade trees
Shade cloth
No dyes!!!
Reduce the wind speed
Shade trees
Curtains
INCREASE
SUPPLY

## Slide 20: Pond Covers
Kick the Devil out of town! Change the geometry of your pond by eliminating the surface area!
Shade Balls
Aqua Caps
Azolla doesn’t count!
INCREASE
SUPPLY

## Slide 21: Pond Covers II
Ponds can be sealed with chemical covers
WaterSavr – 20% savings with 3 applications per week. With a 5 AF pond this is 1/3 AF of water savings.
Aquatain https://aquatain.com
Vegetable Oil
INCREASE
SUPPLY

## Slide 22: Pond Covers III
Change the geometry: Eliminate half of our surface area with floating “tarps”? Assume:
$2000 to cover half of a 5AF pond
50% evaporation reduction.
Water savings = 0.8AF/annual for 5 years
= $500/AF saved.
INCREASE
SUPPLY

## Slide 23: Partnership
Coho as a blessing … introducing farmers to new partnerships for common goals.
  RCD, Nature Conservancy
  Projects to build storage
  Regulatory common sense
  Connections with grant funding
INCREASE
SUPPLY

## Slide 24: Learning From Each Drought
For Anderson Valley water security might actually be improving with each drought
SUMMARY

## Slide 25: Summary Drought 2022
Unlikely to be a “crisis” in Anderson Valley
Probably a “sqeeze” year for some
Definitely a marketing opportunity
SUMMARY

## Slide 26: Droughts Make Great Wine
SUMMARY